## Slide 1
1
Embedded processor
علی مجیدی
8604664
1
دانشگاه صنعتی اصفهان
دانشکده برق و کامپیوتر

## Slide 3: Atmel
Atmel Corporation, founded in 1984
Headquarters San Jose, California, USA
focus on flash microcontrollers
secured products, RF and automotive integrated circuits
Revenue ▼$1.57 billion USD (2008)
Net income ▼$27.2 million USD (2008)
Employees 6,000

## Slide 4: Atmel(ARM)
ARM-based Microcontrollers

## Slide 5: Atmel(ARM)
AT91SAM9 Series
  the same programming model as ARM7-based
  It supports deterministic, real-time operation
  ARM926EJ-S processor
  210 MIPS with a 190 MHz clock
  8K bytes of SRAM and 32K bytes of ROM
  USB Full /high Speed Host and Device interfaces, a 10/100 Base T Ethernet MAC
  USARTs, Synchronous Serial Controllers (SSC), Master/Slave Serial Peripheral Interfaces (SPI), a three-channel 16-bit Timer Counter (TC), a Two Wire Interface (TWI) and four-channel 10-bit ADC

## Slide 6: Atmel(ARM)
AT91SAM9XE Series
  the same programming model as ARM7-based
  It supports deterministic, real-time operation
  ARM926EJ-S processor
  210 MIPS with a 190 MHz clock
  8K bytes of SRAM and 32K bytes of ROM
  USB Full Speed Host and Device interfaces, a 10/100 Base T Ethernet MAC
  USARTs, Synchronous Serial Controllers (SSC), Master/Slave Serial Peripheral Interfaces (SPI), a three-channel 16-bit Timer Counter (TC), a Two Wire Interface (TWI) and four-channel 10-bit ADC
  Peripheral DMA Controller (PDC):(This industry-leading distributed DMA architecture ensures that internal data transfers occur at maximum possible bandwidth with minimal processor intervention)

## Slide 7: Atmel(DIOPSIS)
DIOPSIS® (ARM + DSP)
  is a dual-core processing platform
  integrating a floating-point Magic DSP™ and an ARM926EJ-S RISC microprocessor
  40-bit floating-point provides high dynamic range
  2.3 Mbit of internal memories
  full speed USB host/device, Ethernet MAC, 4xSSC, 3xUSART, 2xSPI, Time Counter, 2xTWI, 2xCAN, Multimedia Card Interface
  1 billion floating point operations per second from the DSP, plus 220 MIPS from ARM

## Slide 8: Atmel(DIOPSIS)

## Slide 9
Founded Cambridge, Massachusetts (1965)
Products Semiconductors
company specializing in data conversion and signal conditioning technology
Revenue $2.6 billion USD (2008)
Employees 8,500 (2009)

## Slide 10: Analog device (ADSP-21xx)
ADSP-21xx
  Compatible DSP with performance up to 160MHz
  Ideal for speech processing and voice-band modems ,as well as real-time control application
  cheap ($10~$15)
  75 MIPS Sustained Performance
  Single-Cycle Instruction Execution

## Slide 11: Analog device (ADSP-21xx)
FEATURES
  3-Bus Architecture Allows Dual Operand Fetches in Every Instruction Cycle
  80K Bytes of On-Chip RAM
  16K Words Program Memory RAM
  16K Words Data Memory RAM
  Two Independent Data Address Generators
  Flexible I/O Structure Allows 2.5 V or 3.3 V Operation
  16-Bit Internal DMA
  Automatic Booting of On-Chip Program Memory
  4 MByte Memory Interface for Storage of Data Tables

## Slide 13: Analog device (ADSP-21xx)
The processor contains three independent computational units:
  the ALU(16 bit , standard set of arithmetic and logic operations and division)
  the multiplier/accumulator (MAC)
  the shifter
BUS
  Program Memory Address (PMA) Bus
  Program Memory Data (PMD) Bus
  Data Memory Address (DMA) Bus
  Data Memory Data (DMD) Bus
  Result (R) Bus

## Slide 14
ADSP-21xx Family |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Performance |  | Packaging & Temp Range |  | Memory |  |  | Peripherals |  |  |  |  | Development Tools | 
 | Clock Speed MHz (Max) | External (IO) Supply Voltage | Package | Temp Range | Program RAM Words | Data RAM Word (KWords) | Ext. Memory Bus (Bits) | Timers | Host Port | SPORT | SPI/UART | ADC | Evaluation Board | Development Software
 |  |  |  |  | (KWords) |  |  |  |  |  |  |  |  | 
ADSP-21990 | 160 | 3.3 | 176 LQFP, 196 CSP_BGA | Industrial | 4 | 4 | 24 | 3 | Yes | 1 | Yes | 14 bit Dual Ch, 20 MSPS | 21992 EZ-KIT Lite | VisualDSP++
ADSP-21991 | 160 | 3.3 | 176 LQFP, 196 CSP_BGA | Industrial | 32 | 8 | 24 | 3 | Yes | 1 | Yes | 14 bit Dual Ch, 20 MSPS | 21992 EZ-KIT Lite | VisualDSP++
ADSP-21992 | 160 | 3.3 | 176 LQFP, 196 CSP_BGA | Industrial | 32 | 16 | 24 | 3 | Yes | 1 | Yes | 14 bit Dual Ch, 20 MSPS | 21992 EZ-KIT Lite | VisualDSP++
ADSP-2191M | 160 | 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 32 | 32 | 16 | 3 | Yes | 3 | Yes | 0 | 21992 EZ-KIT Lite | VisualDSP++
ADSP-2196M | 160 | 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 8 | 8 | 16 | 3 | Yes | 3 | Yes | 0 | 21992 EZ-KIT Lite | VisualDSP++
ADSP-2188N | 80 | 1.8, 2.5, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 48 | 56 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++
ADSP-2189N | 80 | 1.8, 2.5, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 32 | 48 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++
ADSP-2187N | 80 | 1.8, 2.5, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 32 | 32 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++
ADSP-2185N | 80 | 1.8, 2.5, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 16 | 16 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++
ADSP-2186N | 80 | 1.8, 2.5, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 8 | 8 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++
ADSP-2184N | 80 | 1.8, 2.5, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 4 | 4 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++
ADSP-2188M | 75 | 2.75, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 48 | 56 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++
ADSP-2189M | 75 | 2.5, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 32 | 48 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++
ADSP-2185M | 75 | 2.5, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 16 | 16 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++
ADSP-2186M | 75 | 2.5, 3.3 | 144 LQFP, 144 CSP_BGA | Industrial, Commercial | 8 | 8 | 24 | 1 | Yes | 2 | No | 0 | 2189M EZ-KIT Lite | VisualDSP++

## Slide 15: Analog device (Blackfin Embedded Processor)
Application
  Multi-format audio
  Video
  Voice and image processing
  Multi-mode baseband and packet processing
  Control processing
  Real-time security
16-/32 bit embedded processor

## Slide 17: Analog device (Blackfin Embedded Processor)
Data arithmetic unit
  Two 12-bit MACs(the multiplier/accumulator )
  Two 40-bit ALUs
  Four 8-bit video intrface
  Single barrel shifter
Address arithmetic unit
  Memory fetch
  Index,length,base,and modify registers
  Circular buffering

## Slide 18: ADSP-BF512

## Slide 19: ADSP-BF512
FEATURES
  Up to 400MHz high-performance Blackfin® processor
  Two 16-bit MACs, two 40-bit ALUs, four 8-bit video ALUs,
  40-bit shifter
  168-ball CSP_BGA
  176-lead LQFP with exposed pad
  IEEE 802.3-compliant 10/100 Ethernet MAC
  Parallel peripheral interface (PPI),
  2 dual-channel, full-duplex synchronous serial ports
  (SPORTs), supporting 8 stereo I2S channels
  12 peripheral DMAs, 2 UARTs, 32-bit core timer
  On-chip PLL capable of 0.5to 64 frequency multiplicatio
  EZ-kit
    ASDP-BF533
    AD1836 96Khz audio codec
    ADV7171 video encoding
    2MB flash memory

## Slide 20: Analog device (SHARC)
SHARC
  Floating point DSP
  At 200 MHz (5 ns) core instruction rate, 1200 MFLOPS (Million Floating Point Operation Per Second) peak/800 MFLOPS sustained
  2M bits on-chip dual-ported SRAM
  Up to 4M bits on-chip dual-ported mask-programmable ROM
  Transfers between memory and core at up to four 32-bit floating- or fixed-point words per cycle, sustained 2.4 Bps bandwidth at 200 MHz core instruction rate; 900 Mbps is available via DMA
  Serial peripheral interface (SPI) , PLL has a wide variety
  Price($180~$270)

## Slide 22
Founded in Silicon Valley in 1984 and headquartered in San Jose, California
Headquarters: San Jose, California
Industry :Integrated Circuits
Products:FPGAs, CPLDs
Revenue: $1.91 billion (2008)
Employees:3,100

## Slide 23: Xilinx(Embedded Processing )
Solutions
  High performance PowerPC® 440 and PowerPC 405 32-bit hard processors
  Flexible 32-bit MicroBlaze™ soft processor
  Award winning Platform Studio and the Embedded Development Kit (EDK)

## Slide 24: Xilinx(PowerPC)
PowerPC Hard Processor
  The IBM PowerPC 440 and 405 cores are hard 32-bit RISC CPU processors immersed directly into the Xilinx Virtex FPGA fabric to implement high performance embedded applications
  The PowerPC 440 is incorporated in the Virtex-5 FXT
    128-bit interfaces and point-to-point connectivity
    Integrated DMA channels
    Processor Local Bus (PLB) interfaces minimize logic
  The PowerPC 405 is supported in both the Virtex-4 and Virtex-II Pro
    memory management unit (MMU)
    -stage pipeline

## Slide 25: PowerPC 405(Virtex-4 FX FPGAs)
Virtex-4 FX FPGA Benefits
  Implement high speed serial connectivity with RocketIO™ serial transceivers
    Up to 24 transceivers, each providing 622 Mbps to 6.5 Gbps, full duplex operation
    Enable flexible bridging between emerging serial standards and existing parallel standards
  Provides unique tri-mode Ethernet Media Access Controller (MAC) blocks for guaranteed performance
    10/100 Mbps mode, 1000 Mbps mode, 10/100/1000 Mbps mode
  Accelerate processing performance with IBM PowerPC™ 32-bit RISC processor with APU controller
    700+ DMIPS @ 450 MHz; up to 1,400+ DMIPS in a single FPGA with two processors
    Low power consumption: 0.45 mW/MHz
    Auxiliary Processor Unit (APU) controller makes it easy to integrate hardware accelerators

## Slide 26: Virtex-4FPGAs
Summary of Virtex-4 Family Features
  Digital clock manager (DCM) blocks
  Additional phase-matched clock dividers (PMCD)
  Differential global clocks
  Optional pipeline stages
  Built-in Accumulator (48-bit) and Adder/Subtracter
  Distributed RAM &SDRAM
  Optional programmable FIFO logic automatically

## Slide 27: Virtex-4 FX
System Blocks Specific to the Virtex-4 FX Family
  RocketIO Multi-Gigabit Transceiver (MGT)
    Full-duplex serial transceiver (MGT) capable of 622 Mb/s to 6.5 Gb/s baud rates
    CRC generation and checking
    Programmable TX pre-emphasis or pre-equalization
    On-chip RX AC coupling
  PowerPC 405 RISC Core
    Embedded PowerPC 405 (PPC405) core
    Up to 450 MHz operation
    Five-stage data path pipeline
    16 KB instruction cache
    16 KB data cache
    Enhanced instruction and data on-chip memory(OCM) controllers
    Additional frequency ratio options between PPC405 and Processor Local Bus
  Auxiliary Processor Unit (APU) Interface for directconnection from PPC405 to coprocessors in fabric
    APU can run at different clock rates
    4-cycle cache line transfer
  Tri-Mode Ethernet Media Access Controller
    IEEE 802.3 compliant
    Operates at 10, 100, and 1,000 Mb/s
    Supports tri-mode auto-detect
    Flexible, user-configurable host interface

## Slide 28: Virtex-5
Optimized for embedded processing, DSP, and memory-intensive applications with highest-speed serial I/O
Up to two PowerPC® 440 processors with 32-bit RISC cores, each in its own embedded peripheral block
Enable higher levels of DSP integration and lower power consumption with up to 320 DSP48E slices
  25 x 18, two’s complement, multiplication
  Optional pipelining

## Slide 29: Xilinx(DSP)
Virtex-DSP and Spartan-DSP Series
  Virtex-6 SXT Devices
  Spartan-6 LXT Devices
  Virtex-5 SXT Devices
  Spartan-3A DSP Devices
XtremeDSP Video Starter Kit — Spartan-3A DSP Edition
  evaluate Xilinx FPGA(s) in a wide range
  of Video and Imaging applications
  $1,595
  EDK(application)& system genarator

## Slide 30: MicroBlaze Processor
KCPSM3
Thirty-two 32-bit general purpose registers
32-bit address bus

## Slide 31
Nios II Processor
  Create an exact mix of peripherals, memory interfaces, and hardware accelerators for your application
Cortex-M1
  The ARM Cortex-M1 processor addresses the need for a high-quality, standard processor architecture for Altera® FPGA applications allowing you to choose the optimal implementation for each project
V1 ColdFire (freescale)
  The small-footprint V1 ColdFire core is designed for entry-level 32-bit applications. It enhances system utilization, resulting in low-power consumption, while giving more than ten times the performance of an 8-bit MCU

## Slide 32: Altera( Nios II Processor)
Choose the exact set of CPUs, peripherals, and interfaces needed for your application
Lower overall cost, complexity, and power consumption—combining many functions onto one chip
Increase performance without changing your board design—accelerating only functions that need it
Nios II processors offer you tremendous flexibility
Using SOPC Builder and included embedded peripherals, you create the exact set of peripherals, memories, and I/O circuitry needed for any application, even configurations not available in off-the-shelf processors

## Slide 33: Altera( Nios II Processor)
Standard Peripherals
  The Nios II processor includes a library of commonly used peripherals and interfaces that are available
    JTAG UART
    Common Flash Interface
    UART
    Interval Timer
    Parallel I/O (PIO)
    Serial Peripheral Interface (SPI)
    DMA Controller
    SDRAM Controller :
    On-chip ROM and RAM
    SDRAM, SSRAM, SRAM,
    and flash
    Memory Interfaces
    Ethernet Port

## Slide 34: Altera(Cortex-M1)
Features
  Streamlined three-stage 32-bit ARM® Cortex processor
  Optimized for implementation in FPGAs, targets Altera Cyclone® III FPGAs
  Supported by a wide variety of tools and operating systems in the ARM Connected Community
  Tightly coupled memories for rapid access to on-chip block RAM
  Optional debug, breakpoint, and watchpoint unit
  Configurable Tightly Coupled Memories

## Slide 35: Altera(V1 ColdFire)
Features
  1-pin background debug mode (BDM), real-time debug (RTD) support, works with existing ColdFire debugging tools
  Optimized for the Altera® Cyclone® III FPGAs
  $0 licensing fee and $0 royalty for the core
  Fully synthesizable core
  16 user-accessible, 32-bit wide general-purpose registers
  Independent, decoupled pipelines
  FIFO instruction buffer provides decoupling
  2-stage instruction fetch pipeline (IFP)

## Slide 36
VIA VX800
  The VIA VX800 media system processor is an all-in-one
  800/400MHz FSB
  Supports up to two 64-bit DDR2 667 DIMMs (4 GB max)
  Up to 32-bit sample depth at 192 kHz sampling rate
  Supports three codecs and eight streams
  250MHz engine clock
  128-bit 2D engine with hardware rotation capability
  Up to 256 MB frame buffer
  18-bit TTL LCD interface
  Multiplexed with UART and IR ports
  Supports SATA 2.0 interface
  Supports PCI-Express one 4-lane and two 1-lane ports
  Supports six USB 2.0 ports
VIA VX855 zdf
VIA Eden™ and Eden™ ULV Processors

## Slide 37
Thank you
Question?