## Slide 1: Challenges To Cognitive OFDM Systems
عادل آقاجان
دانشگاه صنعتي اصفهان
دانشکده برق و کامپيوتر
Advisor:
Dr. M.J. Omidi

## Slide 2: Challenges To Cognitive OFDM Systems
• intercarrier
Interference(ICI)
• peak-to-average-power
ratio (PAPR)
• Synchronization
• ...
• Spectrum sensing
• Cross-layer adaptation
• Interference avoidance
• ...
OFDM
challenges
Cognitive radio challenges

## Slide 3: Challenges To Cognitive OFDM Systems
Multiband OFDM system design
Location awareness
Signaling the transmission parameters
Synchronization
Mutual interference

## Slide 4: Multiband OFDM System Design
total bandwidth is divided into smaller bands
Disadvantage of single-band OFDM (wide band) :
  The building of highly complex RF circuitry
  High speed analog-to-digital converters
  higher complexity channel equalizers
For OFDM-based CR, the question is when to use multiband and when to use single band.
Multiband OFDM is employed in UWB.
The challenges that face the implementation :
  wide-range frequency synthesizers
  broadband circuits
  …

## Slide 5: Location Awareness
Applications utilizing location information can be grouped into four categories:
  Location-based services
    Example: monitoring real-time traffic
  location-assisted network optimization
    Example: location-assisted dynamic spectrum access systems
  location-assisted transceiver algorithm optimization
    Example: location-assisted link adaptation
  location-assisted environment sensing
    Example: location-assisted channel environment identification
Pilot sequences which are commonly used in OFDM systems for synchronization, can be used for tracking of unit locations.

## Slide 6: Signaling The Transmission Parameters
Distributing information among communication units, rather than using local sensing:
  reduces the complexity
  improves the performance of the system
Approach:
  Exchange measured information and transmission parameters among cognitive units with usage of licensed channel .
    Disadvantage:
      As the number of units in the same cell increases, the amount of information that must be distributed increases as well.
      The ability of cognitive units to operate adaptively within any given unlicensed band becomes dependent on the availability of such a channel.

## Slide 7: Signaling the transmission parameters (cont.)
Other approach:
  Sending a vector containing disabled subcarriers rather than by sending the spectrum sensing results.
  The deactivation of subcarriers is performed over a block of subcarriers instead of individual subcarriers.
    Disadvantage:
      Probability of interfering is high

## Slide 8: Signaling The Transmission Parameters (cont.)
An Innovative approach:
  Tone-boosting:
    All the terminals modulate a complex symbol at maximum power on those OFDM subcarriers representing the subbands newly allocated by the licensed system.
    All other OFDM subcarriers are modulated with no signal.
    If this is carried out simultaneously by all participating terminals, the access point receives a superposition of the original transmit signals of the licensed users and the OFDM signals of the terminals of the rental system :
      power amplification of the newly allocated subbands
      extremely high detection probabilities

## Slide 9: Tone-boosting(cont.)
This signal interfere with licensed system.
But simulation results have shown that only 10 μs is enough to achieve reliable distributed detection.
Plus, only new accesses of licensed users are affected.

## Slide 10: Synchronization
Synchronization has a large relevance in an OFDM system as this modulation technique is very sensitive to phase noise, frequency offset and timing errors.
With the introduction of CR, conventional synchronization methods become insufficient.

## Slide 11: Synchronization(cont.)
It consists of ten short training symbols (sts) and two long training symbols (LTS) separated by a guard interval (GI).
  Usage:
    signal detection
    automatic gain control
    carrier sensing
    estimation of the frequency
    estimation of the clock offsets
Preamble structure of an IEEE802.11a data packet

## Slide 12: Synchronization(cont.)
Problem of synchronization :
  The NBI(narrowband interference) can interfere with the preamble.
  Preamble can fall into unusable subcarriers.
Solution:
  Longer preambles are required in CR-OFDM systems.

## Slide 13: Mutual Interference
The side lobes of modulated OFDM subcarriers are known to be large.
Mutual Interference :
  Used subcarrier power leaks to nulled subcarriers, which causes interference to LUs.
Solution:
  Windowing in time domain(raised cosine window)
    Disadvantage:
      Reduction of spectral efficiency
  Increase the number of nulled subcarriers(neighboring subcarriers)
    Disadvantage:
      Reduction of spectral efficiency

## Slide 14: Mutual Interference(cont.)
Other solution :
  Active Interference Cancellation :
    Instead of disabling subcarriers adjacent to spectrum holes, a much smaller number of those adjacent subcarriers is used to reduce the interference leaked to spectrum holes.
    Disadvantage:
      Increase complexity

## Slide 15: Mutual Interference(cont.)
Case I:
  Subcarriers 23 through 29 are disabled.
  CP is 8 samples
  Spectrum hole with a 15-dB depth
Case II:
  Raised cosine window
  Roll-off factor of 0.25
  Subcarriers 23 through 29 are disabled.
  CP is 64 samples(orthogonality)
  Spectrum hole with a 30-dB depth
Case III:
  Third method
  CP is 8 samples
  Subcarriers 25 to 27 are disabled
  Subcarriers 23, 24, 28, and 29 are used as cancellation subcarriers.
  Spectrum hole with a 70-dB depth

## Slide 16: Thanks for your attention